## Slide 1
C02 종합 판정
작성: 2026-04-30 23:32 KST | 절대 기준: Doc/TDC-GPX-Datasheet.pdf | 상세 근거: Readiness Review v001
조건부 GO
C02 내부는 닫힘
I-Mode single
28-bit / 200 MHz
Handoff
통합 계약 유지
C02는 expected-count final 계약으로 GPX IFIFO를 empty-read 없이 drain하고, timing legality / CDC / tuser / stale-ready 검증을 통과했다.
닫힌 범위
OP-C02-01~06 PASS
상속 기준
Datasheet READ 40 MHz
후속 항목
full_int packing / output CDC
No-Go 조건: 다음 Cluster가 실제 echo_receiver full_int end-to-end 연결을 C02 closure 필수조건으로 요구하는 경우

## Slide 2
Cluster2 Pipeline
shot 소유권 -> expected 확정 -> GPX drain -> raw/downstream stream
laser_ctrl
fire count
face_seq
shot count
stop_cfg_decode
fire match
expected
CDC tuple
chip_run
latch/check
chip_ctrl
response skid
Datasheet
READ timing
bus_phy
RDN/D[27:0]
raw_cdc
SYNC or ASYNC
decode/cell/output
tuser verified
중요한 경계: expected tuple은 AXIS clock에서 TDC clock으로 atomic CDC되고, raw data는 TDC clock에서 AXI-Stream clock으로 CDC된다.

## Slide 3
상태머신 관계도
C02는 face_seq, stop_cfg_decode, chip_run, chip_ctrl가 역할을 나누어 닫는다
shot_start_gated
current_fire_count
ST_CAPTURE
range window
expected final
fire-count match
IrFlag
I-Mode single end
LATCH
DRAIN_CHECK
EF1 READ
EF2 READ
SETTLE
DONE CTRL
ALU / RECOVERY
ST_DRAIN_LATCH는 expected tuple을 snapshot한다. ST_DRAIN_SETTLE은 expected wait가 아니라 READ 후 EF/status settle guard이다.

## Slide 4
Timing Diagram
Datasheet READ timing과 expected-count drain timing을 분리해서 판단
Bus READ @200 MHz
tick0
ADR
tick1
RDN↓
tick2
tick3
sample
tick4
RDN↑
tick5
rsp
RDN low width = 15 ns, capture delay = 15 ns
Burst READ II = 25 ns = 40 MHz max
Expected-count Drain
shot_start
stop_evt
running
fire final
match
IrFlag
LATCH
READ N
top 검증: physical=expected+1 조건에서도 read=expected, leftover=1 -> EF fallback이 아니라 count-known drain

## Slide 5
Latency / Throughput / II
측정값은 bus-level과 stream-level을 분리해서 해석
구간
측정/계약
값
판단
T0->T1a
IrFlag -> first raw valid
16 clk
내부 first-valid latency
T0->T1b
IrFlag -> first accepted
40 clk
TB backpressure 포함
T0->T7
IrFlag -> output done
428 clk
56 data word drain
Bus READ II
ticks*div*Tclk
25 ns
Datasheet 40 MHz 만족
Raw II
output accepted interval
1..15 clk
FIFO/skid 방출 포함
Throughput
56 word / 428 clk
약 26.2 Mword/s
전체 overhead 포함
first_valid=16clk
first_accept=40clk
II_min=1clk
II_max=15clk
run_complete=427clk
output_done=428clk

## Slide 6
검증 완성도
OP-C02-01~06은 PASS evidence로 닫힘
OP-C02-01
forced empty/tuser negative
CLOSE
OP-C02-02
PH_RESP_DRAIN stuck/fatal
CLOSE
OP-C02-03
expected CDC/top integration
CLOSE
OP-C02-04
downstream tuser boundary
CLOSE
OP-C02-05
timing legality matrix
CLOSE
OP-C02-06
stale-ready boundary
CLOSE
68 pass
0 fail
read=2
leftover=1
blocked accepts=6
order kept
상세 로그 위치: Readiness Review v001 section 9.2

## Slide 7
다음 Cluster 인계
GO 판정과 함께 넘겨야 할 계약
받아야 할 계약
I-Mode single / 28-bit / 200 MHz
count-known drain
fire-count final expected tuple
후속 검토
output CDC / echo packing
항목
다음 단계 처리
C02 판정
근거
output CDC
C03/C04 구조 판단
Handoff
raw_cdc는 검증됨
echo_receiver
full_int packing 정합
Handoff
top/config path는 PASS
OEN
연결/High 고정 검토
Handoff
Low fixed 금지
16-bit bus
28-bit close 이후
Excluded
현재 unsupported
결론: C02 내부 closure 기준으로는 다음 Cluster 진입 가능. 단, 통합 항목은 명시적으로 인계해야 한다.