## Slide 1
C02 보완 결과 v002
한글 UTF-8 재생성본: drain guard / empty-read 방지 / AXI tuser 계약
Count-known
expected count hard bound
Count-unknown
EF fallback single-read
TB strict monitor
empty read = FAIL
결론: Datasheet 기준으로 모델 FIFO occupancy=0 상태의 Reg8/Reg9 read를 1회라도 실패 처리하도록 보강했다.
xsim PASS: total_raw_words=231 / empty-read=0 / tuser-error=0 / IFIFO1-done=14 / final-done=16
근거: TDC-GPX-Datasheet.pdf / C02 Code Fix Plan v004 / xsim tb_tdc_gpx_chip_ctrl PASS
1

## Slide 2
Drain Decision Model
ST_DRAIN_CHECK에서 expected count와 EF sync를 분리 판단
ST_DRAIN_CHECK
expected != 0
drain_cnt < expected
READ allowed
expected = 0
EF_sync = 0
single READ
EF_sync = 1
or count reached
IFIFO done
주의: expected=0은 현재 count-unknown fallback encoding이다. known-zero를 닫으려면 valid 계약이 추가로 필요하다.
근거: TDC-GPX-Datasheet.pdf / C02 Code Fix Plan v004 / xsim tb_tdc_gpx_chip_ctrl PASS
2

## Slide 3
EF Fallback Timing
200 MHz 기준 tS-EF + synchronizer + decision guard
RDN fall
GPX EF update
2-FF sync
guard 5 clocks
next decision
tS-EF max 11.8 ns
5 clocks = 25 ns
RTL: g_EF_SYNC_GUARD_CLKS = 5
검증: fallback [2b]
data=5, empty-read=0
근거: TDC-GPX-Datasheet.pdf / C02 Code Fix Plan v004 / xsim tb_tdc_gpx_chip_ctrl PASS
3

## Slide 4
RTL Patch Map
변경 파일과 역할
tdc_gpx_chip_run.vhd
EF guard generic, expected hard bound, mismatch 판단 분리
tdc_gpx_chip_ctrl.vhd
control beat ID semantic 고정: ififo1_done=0, final_done=1
tdc_gpx_raw_event_builder.vhd
tuser[15:11] shot_seq 주석 정합화
tdc_gpx_cell_builder.vhd
입력 tuser[15:11] shot_seq 주석 정합화
근거: TDC-GPX-Datasheet.pdf / C02 Code Fix Plan v004 / xsim tb_tdc_gpx_chip_ctrl PASS
4

## Slide 5
TB Monitor Upgrade
기능 검증 경계가 PASS/FAIL로 직접 닫히도록 강화
Chip model
occupancy_before_read
Reg8/Reg9 read
when fill=0
ASSERT ERROR
empty_read_cnt++
raw data beat
raw control beat
ID class monitor
tuser contract
[16] global monitor: empty-read=0, raw tuser error=0, control IDs observed
근거: TDC-GPX-Datasheet.pdf / C02 Code Fix Plan v004 / xsim tb_tdc_gpx_chip_ctrl PASS
5

## Slide 6
xsim Result
tb_tdc_gpx_chip_ctrl 단위 검증 결과
[2] Legacy count-known
12 data
PASS
[2b] EF fallback
5 data
PASS
[3] Burst drain
24 data
PASS
[4] drain cap
16 data
PASS
[7] EF empty
0 data
PASS
[9a]/[9b] edge
2 / 64 data
PASS
[16] monitors
empty=0, tuser=0, IDs 14/16
PASS
최종 로그: *** ALL TESTS PASSED *** (total_raw_words=231)
근거: TDC-GPX-Datasheet.pdf / C02 Code Fix Plan v004 / xsim tb_tdc_gpx_chip_ctrl PASS
6

## Slide 7
Remaining Contracts
C02 이후에도 추적해야 할 항목
expected=0은 count-unknown fallback encoding. known-zero는 valid 계약 필요
config_ctrl/top integration에서 expected count CDC와 downstream stream 전파 추가 확인
250 MHz retiming은 제외. 본 결과는 200 MHz 기준
OEN은 connected / High fixed 계열만 후속 검토
근거: TDC-GPX-Datasheet.pdf / C02 Code Fix Plan v004 / xsim tb_tdc_gpx_chip_ctrl PASS
7