## Slide 1
C06 -> C07 Handoff v002
GO_WITH_HARDENED_CONTRACT
C06 closed
control/status/recovery
C07 must close
system timing
SW must accept
16-bit hit slot
Board must close
STA / reserve
archive: sim_results/vivado_xsim/sessions/260514144755_c06_v006_hardening/

## Slide 2
C06 Closed Contracts
다음 단계가 그대로 받아야 하는 닫힌 계약입니다.
ID
계약
근거
H2-03
output width 32/64/128
baseline PASS
H2-04
32/64/128 force/soft recovery
v006 recovery PASS
H2-05
bounded backpressure width sweep
line 143/145
H2-06
rise-only/fall-only output stall
64-bit lane PASS
H2-07
Hit[16] final stream 폐기
SW parser contract
H2-08
sticky clear map
soft_clear vs reset-only
근거: C06_Control_Status_Integration_260514144755_C07_Handoff_v002.md section 2

## Slide 3
C07 System Items
C06 xsim PASS가 시스템 release PASS는 아닙니다.
System ID
항목
이유
SYS-01
VDMA/PS/Ethernet reserve 실측
8 us는 가정값
SYS-02
polygon budget 최종 거리표
810 m @ 8 us margin 부족
SYS-03
SW parser 16-bit hit slot
Hit[16] 폐기 수락 필요
SYS-04
board STA / constraints
xsim 범위 밖
SYS-05
장기 output stall policy
bounded stall만 검증
권고: 다음 Cluster는 C07_System_Integration 또는 C07_Release_Readiness

## Slide 4
Data / Timing Handoff
C06은 final AXIS와 status를 시스템 소비자에게 넘깁니다.
C06 RTL/xsim
closed
final AXIS
32/64/128
SW parser
16-bit hit
system timing
reserve/STA
Metric
인계값
recovery CDC
4 clk / 20 ns
throughput
32:72, 64:44, 128:38 beats/run
conservative T2->T5
32:0.540 us, 64/128:0.500 us
bounded stall
bp_gap=17 pass
C07은 시스템 소비자 관점에서 reserve와 parser를 닫음