## Slide 1
C06 Result v006
Release hardening regression closed
PASS
32/64/128 recovery
PASS
width backpressure
PASS
lane stall
CONTRACT
system reserve
Archive: sim_results/vivado_xsim/sessions/260514144755_c06_v006_hardening/
생성 2026-05-14 14:47:55 KST | artifact count 65

## Slide 2
Plan ID Closure
v006 계획을 PASS, contract, document audit으로 분리해 닫았습니다.
Plan
결과
근거
FP6-01
Recovery width sweep PASS
32/64/128 force/soft
FP6-02
Backpressure width PASS
32/64/128 bp_gap=17
FP6-03
Reserve sweep 계산 완료
8 us는 system measurement
FP6-04
Marker audit 문서화
source/dest/effect 기준
FP6-05
Hit[16] 계약화
16-bit slot / SW parser
FP6-06
Sticky map 확정
soft_clear vs reset-only
FP6-07
Lane stall PASS
rise-only/fall-only
근거: C06_Control_Status_Integration_260514144755_Code_Fix_Result_v006.md section 4

## Slide 3
Recovery Width Sweep
각 width에서 source, destination, effect, output preservation marker를 확인했습니다.
Width
force beats/tlast
soft beats/tlast
PASS marker
32
144 / 4
144 / 4
236/238, 244/246
64
88 / 4
88 / 4
236/238, 244/246
128
76 / 4
76 / 4
236/238, 244/246
source pulse
line 142
TDC pulse
line 146
FSM effect
line 148/156
stream PASS
line 236/244
false positive 방지: source + destination + effect + output marker

## Slide 4
Backpressure / Lane Imbalance
bounded stall과 rise-only/fall-only stall 모두 beat/tlast를 보존했습니다.
Scenario
Width
Beats/tlast
Timing
both-lane bp
32
72 / 2
last cycle 5195
both-lane bp
64
44 / 2
last cycle 5189
both-lane bp
128
38 / 2
last cycle 5189
rise-only bp
64
44 / 2
rise last 5189, fall 5187
fall-only bp
64
44 / 2
rise last 5187, fall 5189
bp_gap=17, 2-cycle stall 반복. 장기/무한 stall은 C07 system fault policy 대상입니다.
근거: xsim_c06_v006_top_int_w*_bp*_260514144755.log line 143/145

## Slide 5
Polygon Reserve
8 us reserve 기준 810 m는 C06 보수 worst 계산에서 margin 부족입니다.
Width
T2->T5
6 us reserve
8 us reserve
10 us reserve
32
0.540 us
1101.6 m
801.8 m
502.0 m
64
0.500 us
1107.6 m
807.8 m
508.0 m
128
0.500 us
1107.6 m
807.8 m
508.0 m
판단: 8 us는 RTL/xsim 실측값이 아닙니다. C07에서 VDMA/PS/Ethernet 측정값으로 다시 산출해야 합니다.
PASS 조건: processing + stall <= 13.888889 us - round_trip - reserve

## Slide 6
Handoff Contracts
C06 내부 blocker는 닫혔고, 다음 단계는 system 계약을 닫아야 합니다.
계약
내용
Hit[16]
final VDMA stream에서는 버림. SW는 16-bit hit slot 수락
Sticky
주요 sticky는 err_soft_clear. quarantine_escape는 reset-only
Width
32/64/128 baseline + recovery + bounded backpressure PASS
System
8 us reserve, board STA, 장기 VDMA stall은 C07에서 닫음
결론: GO_WITH_HARDENED_CONTRACT
후속: C06_Control_Status_Integration_260514144755_C07_Handoff_v002.md